## Slide 1: NAWI RO Analysis Progress Report
M. Kawata, W. Kumagai, R. Imoto
Operational Excellence Gr., Project Design Dev.,
Innovation Center, MKHQ, YHQ
February 1st, 2023
SGDC

## Slide 2: Agenda
RO Analytical Policy
LVMWD RO Analysis
Q&A / Discussion

## Slide 3: Subdivided Objective
The objective can be subdivided into the following three stages.
（3）Considering deterioration of RO membrane (the life extension)
（1）Considering permeate water quality and supply flow
（2）Considering clogging status of RO membrane (monitoring the clogging)
Reduce excessive chemical dosage to meet water demand
Cleaning when the clogging status reaches the criteria limit rather than periodically (reduces excessive chemical cleaning)
Continue operation until replacement criteria based on expecting life
(Prevent unnecessary replacement)
(How continue operation and extent to the life if deterioration is severe, etc.)
Optimization of membrane condition fixed
Monitoring membrane condition taking advantage of optimization
1. RO Analytical Policy

## Slide 4: Where to be focusing
Expand the control and considered value step by step.
  Fix to the actual value when optimization calculation if the value is not considered
RO
NaClO
UF
Acid
Potable Water
UV／AOP
UV Radiation with H2O2 or NaClO
Anti-Scalant
Water quality
(1) Considering permeate water quality and supply flow
(2) Considering clogging status of RO membrane (monitoring the clogging)
(3) Considering deterioration of RO membrane (the life extension)
Degree of Clogging
Membrane cleaning
Membrane life
Monitoring membrane status
1. RO Analytical Policy
Given Region
Given Region

## Slide 5: 目的(1)：流入・透過水質を考慮した運転
最適化ポイント：膜前後の水質関係を捉えながら、薬剤コストを削減する
モデリングポイント：膜前のデータから、膜後の水質を予測する
RO膜
NaClO
UF膜
水質調整薬剤
再生水
UV／AOP
UV照射／薬剤
閉塞防止剤
水質需要
膜閉塞度
膜洗浄
膜寿命
水質を予測しながら、操作を決定
RO膜との間で融通可能なら、最適化対象になる？
常にgivenとして扱う範囲
膜後の水質
膜前の水質・量
時間
時間
水量は目標値に追従するように制御されている
1. RO Analytical Policy

## Slide 6: 井本さんのパート
基本的には1st Quarterly Reportから抜粋する
今後のタスクについても記載
2. LVMWD RO Analysis

## Slide 7: 今後の課題
他データの分析と、水質予測モデルや最適化モデルの構築。
2. LVMWD RO Analysis
水質予測／最適化モデルの構築
流量の温度補正
薬液添加量
水質基準などを守る範囲で、
薬液添加量や圧力操作を決定
膜後の水質
膜前のデータ
時間
時間
予測
最適化
流量が一定の図
温度補正された流量イメージ
塩分除去率

## Slide 8: 質疑応答
SGDCから質問を受け付ける
  基本的に井本さんパートに質問してくるはず、川田さんと熊谷でもサポート
イノベから質問する
  SAO Algorithm for UF Process（熊谷、必要性は下がるが）
3. Q&A / Discussion