## Slide 1: Analysis stance
In anticipation of the development of optimization, consider which data groups should be emphasized.
1. Analytical Policy
System
Input/Manipulated
parameter
Output quality
Disturbance
Expressing the input-output relationship of equipment as a characteristic formula
quality
Time t
Time t
Comply with demand and quality required
Disturbance
Time t
Reduce operating costs
Identify disturbances
Formulation for operation planning optimization
Modeling with operational optimization in mind
Calculate the lowest cost operation plan within constraint conditions
Constraints and costs that need to be considered in operation are defined as formulas.
Expressing the input-output relationship of equipment as a characteristic formula
: Comply with the water quality.
: Reduce operating costs
: Each parameters should comply with the characteristic
Data-driven highlighted

## Slide 2: Objective of RO Optimization
Clogging due to fouling Scaling by Crystallization Fouling by deposit
RO
Disinfection/ NaClO
UF
Clogging Prevention/ Anti-Scalant
Potable Water
Chemical costs
Membrane cleaning costs
Water quality and flow rate to be maintained
UV／AOP
Electricity costs
Within the range of maintaining water quality and flow rate, operating costs are minimized considering RO membrane Condition.
  Maintaining high recovery rate, good water quality (high salt rejection), and extending RO membrane life
Control Carcinogens
Chemical costs
Chemical costs
Membrane replacement costs
Oxidation/
UV radiation with Chemical
1. Analytical Policy

## Slide 3: RO Viewpoint for Analysis
What are the operating costs and the associated Control parameters and disturbances?
  Control target: Anti-Scalant, etc.
  Disturbances: inflow water quality, etc.
What are the constraints (parameter to be monitored) to be observed in operation?
  Monitoring parameters: Final water quality, supply flow rate, etc.
What is the timescale of the operation (optimization period, data interval) ?
What mathematical model is needed to relate each variable?
  Relationship between operation parameter and cost
  Relationship between operation parameter, disturbance, and water quality (including RO membrane characteristics)
1. Analytical Policy

## Slide 4: Subdivided Objective
The objective can be subdivided into the following three stages.
（3）Operation when the membrane wear-out (the life extension)
（1）Operation needs to consider final water quality and supply flow rate
（2）In addition, clogging status to be considered (monitoring the clogging)
Reduce excessive chemical dosage to meet water demand
Cleaning when the clogging status reaches the criteria limit rather than periodically (reduces excessive chemical cleaning)
Continue operation until replacement criteria base on expecting life
(Prevent unnecessary replacement) (How continue operation and extent to the life if deterioration is severe, etc.)
Optimization of membrane
condition fixed
Monitoring membrane condition taking advantage of optimization
1. Analytical Policy

## Slide 5: Where to be focussing
Expand the control value to be considered step by step.
  Fix to the actual value when optimization calculation if the value is not considered.
RO
NaClO
UF
Acid
Potable Water
UV/ AOP
Flow rate and quality as required
UV Radiation with
H2O2 or NaClO
Anti-Scalant
Water quality &
flow rate required
（1）Operation needs to consider final water quality and supply flow rate
（2）In addition, clogging status to be considered (monitoring the clogging)
（3）Operation when the membrane wear-out (the life extension)
Degree of Clogging
Membrane cleaning
Membrane life
Monitoring membrane status
Conditions are given
1. Analytical Policy

## Slide 6: Objective (1): Final water quality and flow rate considered
Optimization: Reduce chemical costs within the balance of water quality and flow rate Pre- & Post-RO. Flow rates should be a constant. Modeling: Predict Post-RO quality and flow rate based on Pre-RO data.
RO
NaClO
UF
UV/ AOP
Predict water quality and flow rate and decide values
Subject to be optimization target if interchangeable with RO
Time
Time
Post-RO
Water quality and flow rate
1. Analytical Policy
UV Radiation with
H2O2 or NaClO
Conditions are given
Acid
Potable Water
Flow rate and quality as required
Anti-Scalant
Water quality &
flow rate required
Degree of Clogging
Membrane cleaning
Membrane life
Pre-RO
Water quality and flow rate

## Slide 7: Objective (2): Clogging Status to be Considered
RO
NaClO
UF
UV/ AOP
Optimization: Reduce chemical costs by cleaning based on the clogging status
Modeling: Predict clogging status based on Pre- & Post- RO
Determine cleaning plans while predicting the degree of blockage
Time
Time
ClP
What makes benefit (cost reduction, prevention of less permeability) brought by CIP strategy ?
1. Analytical Policy
Conditions are given
Acid
Potable Water
Flow rate and quality as required
Anti-Scalant
Water quality &
flow rate required
Degree of Clogging
Membrane cleaning
Membrane life
UV Radiation with
H2O2 or NaClO
Differential & Transmembrane
pressure
Clogging status

## Slide 8: Objective (3): RO deterioration to be considered
RO
NaClO
UF
UV/ AOP
Optimization: RO replacement costs are reduced by RO life extension considered
Modeling: Predict the RO deterioration based on Pre- & Post- RO data
Clogging and RO life are significantly different time scale.
1. Analytical Policy
Conditions are given
Acid
Potable Water
Flow rate and quality as required
Anti-Scalant
Water quality &
flow rate required
Degree of Clogging
Membrane cleaning
Membrane life
UV Radiation with
H2O2 or NaClO

## Slide 9: Difference per Objective
Step up from Small to Large and Easy to Difficult
Optimization effect
Small
Middle
Large
Optimization period
Short-term
(minutes to hours)
Mid-term
(days to months)
Long-term
(months to years)
Model strategy
Closer to statistical models
Statistical/ Physical Models
Closer to the physical model
Difficulty
Easy
Middle
Difficult
(1) 最終水質と供給量を考慮
(2) RO膜閉塞状態も考慮
(3) RO膜劣化も考慮
(1) Consider final water quality and flow rate
(2) RO Clogging Consideration
(3) RO Deterioration Consideration
1. Analytical Policy

## Slide 10: Concerns
Optimization model is not compatible, for example, RO deterioration cannot be expressed from hours operation data.
Since membrane state modeling itself is difficult, it may be better to proceed with the following approach
Water Quality Prediction Model
RO clogging status prediction model
RO degradation prediction model
Monitoring RO membrane status
(2) If modeling goes well, reflect to the optimization
(1) Highest priority
(3) If modeling goes well, reflect to the optimization
1. Analytical Policy

## Slide 12: RO Membrane Performance
・・・
Concentrated water (drainage)
Supplied water
Through water
Concentration
Volume flow rate
Conductivity
Recovery rate[%]＝
LRV＝
Logarithmic reduction (virus removal rate)
Ionic substance removal rate
Removal rate
RO Membrane performance
RO Membrane performance is measured in terms of removal rate and recovery rate.
What data needs to be monitored to evaluate membrane performance?

## Slide 13: Fouling and Scaling
・・・
Antiscalent NaOH
Cleaning is necessary because the recovery rate decreases with blockage.
https://www.muro-chem.co.jp/business/chemical/separation_membrane.html
Fouling removal
Scale prevention
Detected by differential pressure between membranes, etc., and periodically physical cleaning (backwashing, etc.)
Remove fouling with chemical cleaning
Pretreatment with chemicals to prevent crystal precipitation
RO In order to maintain membrane performance, cleaning and chemical addition are required.
What operations are necessary to restore membrane performance and prevent deterioration?