## Slide 1: NAWI RO Analysis Progress Report
M. Kawata, W. Kumagai, R. Imoto
Operational Excellence Gr., Project Design Dev.,
Innovation Center, MKHQ, YHQ
February 1st, 2023
SGDC

## Slide 2: Agenda
RO Analytical Policy
LVMWD RO Data Analysis
Q&A / Discussion
Notes: This slide shows today’s agenda. There are three parts, first part is RO analytical policy, I will explain. Second part is Lasvergenes RO Data Analysis, Imoto-san explain. Final part is Q&A/discussion part.

## Slide 3: Objective of RO Optimization
Operating costs are minimized considering RO membrane condition within the range of maintaining water quality and flow rate.
  Maintaining high recovery rate, good water quality (high salt rejection), and extending RO membrane life.
1. RO Analytical Policy
Clogging due to fouling Scaling by crystallization Bio-fouling by deposit
RO
Disinfection/ NaClO
UF
Clogging Prevention/ Anti-Scalant
Potable Water
Chemical costs
Membrane cleaning costs
Water quality and flow rate to be maintained
UV／AOP
Electricity costs
Control Carcinogens
Chemical costs
Chemical costs
Membrane replacement costs
Oxidation/
UV radiation with Chemical
Notes: First, I explain RO data analysis and optimization policy. This shows potable water reuse process. Water from sewage plant is treated by this process and supplied to potable reuse.
It mainly consists of UF, RO, UV, and AOP process units. The objective of RO optimization shows operating costs are ~. There are important costs in many places, for example, chemical cost, RO membrane cleaning cost, and electricity cost. Moreover there are considering conditions in many places, for example, recover rate, water quality, and RO membrane life. So, optimization strategy is to select critical costs and conditions according to priority.

## Slide 4: Subdivided Objective
The objective can be subdivided into the following three stages.
（3）Considering deterioration of RO membrane (the life extension)
（1）Considering permeate water quality and supply flow
（2）Considering clogging status of RO membrane (monitoring the clogging)
Reduce excessive chemical dosage to meet water demand
Cleaning when the clogging status reaches the criteria limit rather than periodically (reduces excessive chemical cleaning)
Continue operation until replacement criteria based on expecting life
(Prevent unnecessary replacement)
(How continue operation and extent to the life if deterioration is severe, etc.)
Optimization of membrane condition fixed
Monitoring membrane condition taking advantage of optimization
1. RO Analytical Policy
Notes: The objective can be subdivided into the following three stages. First stage is considering~, to reduce excessive~. Second stage is considering ~ that is monitoring the clogging, to clean when the clogging status~. Third stage is considering ~ that is the life extension, to~. First stage can be rephrased as optimization of membrane condition fixed. On the contrary, Second and third stages can be rephrased as monitoring membrane condition taking advantage of optimization.

## Slide 5: Focused Region
Expand the control and considered value step by step.
  Fix to the actual value when optimization calculation if the value is not considered
RO
NaClO
UF
Acid
Potable Water
UV / AOP
UV Radiation with H2O2 or NaClO
Anti-Scalant
Water quality
(1) Considering permeate water quality and supply flow
Degree of Clogging
Membrane cleaning
Membrane life
Monitoring membrane status
1. RO Analytical Policy
Given Region
Given Region
Non-Monitoring membrane status
Subject to be optimization target if interchangeable with RO.
(2) Considering clogging status of RO membrane (monitoring the clogging)
(3) Considering deterioration of RO membrane (the life extension)
Notes: Based on the stages, RO analytical policy is to expand the control and considered value step by step. First stage is to control and consider yellow values. Green values are added in second stage and red values are added in third stage as well. But, gray regions are considered as given area in RO optimization, so they are fixed to actual value when calculation.

## Slide 6: Objective (1): Operation considering permeate water quality and supply flow
Optimization: Reduce chemical costs within the balance of water quality and flow rate in Pre & Post-RO.
Modeling: Predict Post-RO water quality and flow rate based on Pre-RO data.
Predict water quality and decide operation values.
Post-RO
Water quality
Pre-RO
Water quality and flow rate
Time
Time
1. RO Analytical Policy
RO
NaClO
UF
UV / AOP
UV Radiation with
H2O2 or NaClO
Acid
Potable Water
Anti-Scalant
Water quality
Degree of Clogging
Membrane cleaning
Membrane life
Flow rate should be constant.
Given Region
Given Region
Predict
Decide
Notes: We try to the first stage now. This is a detailed policy in first stage. Optimization is to reduce chemical costs ~ Post-RO. Modeling is to predict ~. Please have a look at the lower figure. Left is water quality and flow rate in pre-RO. We try to predict water quality in post-RO from left data. After that, we try to decide the best operation values from right data by optimization. So, we need create the quality prediction model and optimization model. This is the end of the explanation of RO analytical policy. I’ll switch to Imoto-san.

## Slide 7: 井本さんのパート
基本的には1st Quarterly Reportから抜粋する
今後のタスクについても記載
2. LVMWD RO Analysis

## Slide 8: 今後の課題
他データの分析と、水質予測モデルや最適化モデルの構築。
2. LVMWD RO Analysis
水質予測／最適化モデルの構築
流量の温度補正
薬液添加量
水質基準などを守る範囲で、
薬液添加量や圧力操作を決定
膜後の水質
膜前のデータ
時間
時間
予測
最適化
流量が一定の図
温度補正された流量イメージ
塩分除去率

## Slide 9: 質疑応答
SGDCから質問を受け付ける
  基本的に井本さんパートに質問してくるはず、川田さんと熊谷でもサポート
イノベから質問する
  SAO Algorithm for UF Process（熊谷、必要性は下がるが）
3. Q&A / Discussion

## Slide 11: Analysis stance
In anticipation of the development of optimization, consider which data groups should be emphasized.
System
Input/Manipulated
parameter
Output quality
Disturbance
Expressing the input-output relationship of equipment as a characteristic formula
Quality
Time t
Time t
Comply with demand and quality required
Disturbance
Time t
Reduce operating costs
Identify disturbances
Formulation for operation planning optimization
Modeling with operational optimization in mind
Calculate the lowest cost operation plan within constraint conditions
Constraints and costs that need to be considered in operation are defined as formulas.
Expressing the input-output relationship of equipment as a characteristic formula
: Comply with the water quality.
: Reduce operating costs
: Each parameters should comply with the characteristic
Data-driven highlighted
Supplementary: RO Analytical Policy
Cost

## Slide 12: Difference per objective
Step up from Small to Large and Easy to Difficult
Optimization effect
Small
Middle
Large
Optimization period
Short-term
(minutes to hours)
Mid-term
(days to months)
Long-term
(months to years)
Model strategy
Closer to statistical models
Statistical/ Physical Models
Closer to the physical model
Difficulty
Easy
Middle
Difficult
(1) 最終水質と供給量を考慮
(2) RO膜閉塞状態も考慮
(3) RO膜劣化も考慮
(1) Consider final water quality and flow rate
(2) RO Clogging Consideration
(3) RO Deterioration Consideration
Supplementary: RO Analytical Policy